## Slide 1
The diagram above shows the geometry of the signals radiated and received by the main and interferometer arrays in the SuperDARN radars. Each array is aligned along the x-axis with increasing antenna number in the +x direction. The radiated and received signals are confined to the quarter-sphere defined by the entire x-axis and the +Y and +Z half-axes. This occurs due to a corner reflector located at a small –y distance behind the antennas and reflections by the ground located at Z=0. The antennas are phased so that there is construction interference of the transmitted and received signals along the black arc that is in contact with the solid blue, green, and red arrows. All of these lines emanate from the origin and lie on the surface of a quarter-cone that has a cone angle of 90-φ0 degrees with respect to the x-axis. This means that each solid colored line has an included angle with the x-axis of 90-φ0 degrees.
For the radars, the direction of the transmitted and received signals are commonly defined relative to the array normal direction by the angle φ0. The transmissions shown here have a –x component of propagation and are assigned a negative azimuth angle. If they had a +x component of propagation, they would be assigned a positive azimuth angle. For the transmissions shown, the only one that is truly propagating at an azimuth of φ0 is the blue transmission that lies in the xy-plane. The red transmission is propagating at φ0 = 90° with an elevation angle, θ, of 90-φ0 degrees. We should note, however that the antennas radiate little or no energy at φ0 = 90° or at θ=0°, so it is unlikely that any backscatter would be observed from the directions of either the blue or red arrows.
Y
X
Z
φ0
90-φ0
θ

## Slide 2
A more interesting case is that associated with the reception of backscatter from the direction of the solid green arrow. It can be seen that the vector can be projected onto the x-axis via the coning angle or it can be projected vertically into the xy-plane, where it has an azimuth angle φ>φ0, and from there, through the angle 90-φ, onto the x-axis. The two approaches give identical results implying that
cos(90-φ0)=cos(θ)cos(90- φ), or
sin(φ0)=cos(θ)sin(φ) → φ=sin-1(sin(φ0)/cos(θ))
This result shows that for every phasing angle φ0 to which the radar is steered, there is broad range of paired {θ,φ} values into which power can be transmitted and from which backscatter returns can be received. It had been realized that the vertical beamwidth of the antenna arrays was quite broad and that the returning signals could extend over a fairly wide range of elevation angles, but it had not been realized that each of these elevation angles was paired with a corresponding different azimuth angle.
The conclusion from this analysis is that interferometry measurements are even more important to the localization of backscatter sources within the radar field of view than had previously been anticipated. The approach is to phase the radar beam into a particular beam azimuth and to use the interferometer capability of the radar to measure the elevation angles of the backscattered signals as a function of range. From this data it is possible to determine the true azimuth for each range where elevation data is available. We now present the methodology for determining the elevation angles of the backscattered data.